The IWG7 4MOST Galactic Pipeline (4GP): Development Report
Dominic Ford, Lund Observatory
21 July 2017

The 4MOST Galactic Pipeline (4GP) is a collection of python modules which wrap spectral synthesis and processing tools including Turbospectrum, 4FS, radial-velocity estimating codes, and the Cannon. A common data format is used for storing spectra and their associated metadata, including the ability to search for spectra by arbitrary metadata constraints. This allows spectra to be easily passed between arbitrary combinations of tools. A simple web interface allows the contents of spectrum libraries to be searched and viewed quickly for diagnostic purposes.

In due course we will use this framework to develop a fully automated pipeline for extracting radial velocities and stellar labels from observed spectra. Presently, we are using it to characterise the accuracy and speed with which the Cannon can operate when tested on noisy spectra.

The code and associated documentation is available on GitHub:

https://github.com/dcf21/4most-4gp
https://github.com/dcf21/4most-4gp-scripts

The Cannon is a data-driven code which uses machine-learning algorithms to learn how each pixel within a spectrum correlates with each label which is to be derived. Label in this context may refer to stellar parameters – Teff, log(g) and [Fe/H] – or the abundances of particular elements.

The Cannon requires a training set of stars with known stellar labels in addition to the test stars whose labels are to be determined.

## Input Spectra
For the purposes of our tests, we use a sample of 1,232 training stars and 1,001 test stars. These are all giant stars with Teff < 5000 K, with elemental abundances known from APOGEE. This sample is identical to the stars used by Casey & Hawkins in their preliminary tests in 2016.

We have used Turbospectrum to synthesise spectra for these stars spanning the wavelength range 3700 A to 9500 A at a spectral resolution of 50,000. This is significantly higher resolution than 4MOST HRS, and is selected so that the output can be reused for arbitrary future tests. Each spectrum takes ~ 7 minutes to synthesise, so resynthesising the complete sample takes roughly 10 CPU days.

The parameter-space coverage of the test and training sets are shown below:

Figure 1: The parameter space coverage of the test and training sets.

To add noise to the synthetic spectra, we use the 4FS Exposure Time Calculator (ETC). This can calculate the length of observation needed to observe each object to any given signal to noise ratio, including a model of the sky transmission and emission at Paranal. It also down-samples the synthetic spectra to the resolution expected from 4MOST, and accounts for the wavelength-dependent sensitivity of each of 4MOST’s detector chips.

The process is illustrated in Figure 2 for one of the test stars in our sample. Panel (a) shows the synthesised flux for the test object, as returned by Turbospectrum. Panels (c) and (d) show the degraded spectra returned by 4FS for 4MOST’s HRS and LRS modes respectively. The three wavelength arms within each mode are shown in different colours.

For each object, the Cannon requires a single spectrum, sampled on a common raster of wavelengths shared with all the input spectra. To achieve this, we stitch the spectra from the three wavelengths arms together, as shown in panels (e) and (f). In the LRS mode, the wavelength arms overlap, and we made the arbitrary decision to splice them at wavelengths of 5327.7 A and 7031.7 A. These splicing points are identical to those used by Casey & Hawkins (2016).

## Defining SNR
The nominal SNR of a spectrum needs to be precisely defined, because the SNR is wavelength dependent. The SNR of the spectrum discussed above is shown in panels (g) and (h) on the next page.

Following Casey & Hawkins (2016), we define the nominal SNR to be the median SNR per pixel in the range 6180 A to 6680 A. This region was chosen because it is common to both LRS and HRS, and it does not fall near the edges of any chips, where the SNR is atypically low.

The nominal SNR of the spectrum shown here is 250.

## Continuum normalisation
The Cannon requires its input spectra to be continuum normalised. Applying continuum normalisation to the output of 4FS is not straightforward, especially at the edges of the chips, where the flux is low.

Turbospectrum produces the input spectra in both continuum-normalised and non-continuum-normalised form, and so as a work-around, we extract the continuum (with no lines) by dividing the latter by the form. Passing this through a separate run of 4FS gives a continuum-only output spectra.

Dividing the spectrum with lines with that without lines gives a perfectly continuum-normalised output.

Figure 2: The process of putting an example synthetic spectrum through 4FS. See the text for details. The star shown here has the APOGEE ID: 2M22552267+5331345.

## Accuracy of the Cannon’s label determination
The plots below show the mean absolute offset of the stellar label values estimated by the Cannon, from those used to synthesise the spectra. This is plotted against the nominal SNR per Angstrom to which the input spectra were degraded. Each data point is an average of all 1,001 test objects.

Grey horizontal lines show the target accuracies for each stellar label, as quoted by Thomas Bensby at the DFDR meeting. These are 0.1-0.2 dex for individual elemental abundances, 100 K for Teff, and 0.3 dex for log(g).

The lines labelled “Ford (External)” are based on spectra which were synthesised and degraded by Dominic Ford as described above. The lines labelled “Hawkins (External)” were constructed by exactly the same method, and using the same sample of stars, but we used the degraded spectra generated by Casey & Hawkins (2016). These plots may slightly differ from their original report, since we have repeated the step of label determination by training the Cannon on their spectra.